Notice: the document's content is according to ap99.

1\ CPU's GMAC0 is connect to switch's PHY4 through RGMII;
2\ CPU's GMAC1 is connect to switch's MAC0 (Here mac0 worked as phy) through GMII;
3\ The GMAC0's base address is 0x1900_0000, and the GMAC1's base address is 0x1A00_0000.
#define athr_gmac_reg_rd(_mac, _reg) \
        (athr_reg_rd((_mac)->mac_base + (_reg)))

#define athr_gmac_reg_wr(_mac, _reg, _val) \
        athr_reg_wr((_mac)->mac_base + (_reg), (_val));

RANGE: 0x000 ~ 0x1D8
Pay Attention To these register:
0x004 MAC Configuration 2
0x058 & 0x05c ETH Configuration 4 & ETH Configuration 5
0x080 ~ 0x098 the Rx/Tx static register

There are also ethernet MAC/PHY port registers, But CPU does not care about it. It does not use these to port.

4\ The control register about GMAC0 and GMAC1, here is the interface that used to access the register
athr_reg_rd() and athr_reg_wr().
#define ATHR_GMAC_ETH_CFG 0x18070000

“The sixth port (port5) supports a PHY interface as a WAN port. The first port (port0) supports a MAC interface and can be configured in MII-PHY or RMII-PHY mode to connect to an external management CPU or an integrated CPU in a routing or xDSL engine.”

There are three classes of registers in switch chip, Global Control Registers, Port Control Registers and MII Registers.

We use the same interface to read/write the Global Control Registers and Port Control Registers. Here are they:
#define phy_reg_read athr_gmac_mii_read
#define phy_reg_write athr_gmac_mii_write
unsigned int athrs26_reg_read(unsigned int s26_addr);
void athrs26_reg_write(unsigned int s26_addr, unsigned int s26_write_data)

here is an example,
athrs26_reg_read(0x104) → …

They use the same MII interface, but reading the normal register is much more complicate, it needs three stages.

We directly use phy_reg_read/ phy_reg_write to read and wirte MII Registers. Here is an example:
phyHwStatus = phy_reg_read(phyBase, phyAddr, ATHR_PHY_SPEC_STATUS);
//phyBase 0, phyAddr 0x1;

Kernel timer(jiffies)
tick_init() → clockevents_register_notifier(&tick_notifier) → raw_notifier_chain_register(&clockevents_chain, nb [tick_notifier]) →
notifier_chain_register(&nh->head, n [tick_notifier])
{
    while ((*nl) != NULL) {
        if (n->priority > (*nl)->priority)
        break;
        nl = &((*nl)->next);
    }
    n->next = *nl;
    rcu_assign_pointer(*nl, n);
    return 0;
}

static struct notifier_block tick_notifier = {
    .notifier_call = tick_notify,
};
static RAW_NOTIFIER_HEAD(clockevents_chain);
/*
 * Atomic notifier chains: Chain callbacks run in interrupt/atomic
 * context. Callouts are not allowed to block.
 * Blocking notifier chains: Chain callbacks run in process context.
 * Callouts are allowed to block.
 * Raw notifier chains: There are no restrictions on callbacks,
 * registration, or unregistration. All locking and protection
 * must be provided by the caller.
 * SRCU notifier chains: A variant of blocking notifier chains, with the same restrictions.
 */
struct notifier_block {
    int (*notifier_call)(struct notifier_block *, unsigned long, void *);
    struct notifier_block *next;
    int priority;
};

struct atomic_notifier_head {
    spinlock_t lock;
    struct notifier_block *head;
};

struct blocking_notifier_head {
    struct rw_semaphore rwsem;
    struct notifier_block *head;
};

struct raw_notifier_head {
    struct notifier_block *head;
};

struct srcu_notifier_head {
    struct mutex mutex;
    struct srcu_struct srcu;
    struct notifier_block *head;
};

init_IRQ() →
        arch_init_irq() → //调用具体板子的函数
        mips_cpu_irq_init() →
**************************************************
        if (cpu_has_mipsmt)
        for (i = irq_base; i < irq_base + 2; i++)
        set_irq_chip_and_handler(i, &mips_mt_cpu_irq_controller, handle_percpu_irq);

        for (i = irq_base + 2; i < irq_base + 8; i++)
        set_irq_chip_and_handler(i, &mips_cpu_irq_controller, handle_percpu_irq);

static struct irq_chip mips_mt_cpu_irq_controller = {
    .name = "MIPS",
    .startup = mips_mt_cpu_irq_startup,
    .ack = mips_mt_cpu_irq_ack,
    .mask = mask_mips_mt_irq,
    .mask_ack = mips_mt_cpu_irq_ack,
    .unmask = unmask_mips_mt_irq,
    .eoi = unmask_mips_mt_irq,
};

static struct irq_chip mips_cpu_irq_controller = {
    .name = "MIPS",
    .ack = mask_mips_irq,
    .mask = mask_mips_irq,
    .mask_ack = mask_mips_irq,
    .unmask = unmask_mips_irq,
    .eoi = unmask_mips_irq,
};
**************************************************
time_init() →
       plat_time_init() //调用具体平台的函数
       mips_clockevent_init() →
        r4k_clockevent_init() →
        cd = &per_cpu(mips_clockevent_device, cpu);
        cd->event_handler = mips_event_handler
        clockevents_register_device(cd) →
        list_add(&dev->list, &clockevent_devices);
        clockevents_do_notify(CLOCK_EVT_NOTIFY_ADD, dev [cd]) →
        raw_notifier_call_chain(&clockevents_chain, reason, dev [cd]) →
        __raw_notifier_call_chain(nh, val, v [cd], -1, NULL) →
        notifier_call_chain(&nh->head, val, v, nr_to_call, nr_calls) →
        nb->notifier_call(nb, val, v) ==
        tick_notify(nb, val, v) →
        tick_check_new_device(dev [cd]) →
        td = &per_cpu(tick_cpu_device, cpu);
-----------------------------(缩进与前一行一致)-----------------------
     tick_setup_device(td, newdev [cd], cpu, cpumask_of(cpu)) →
        td->evtdev = newdev;
        tick_setup_periodic(newdev, 0) →
        tick_set_periodic_handler(dev, broadcast [0] ) →
        dev->event_handler = tick_handle_periodic;
----------------------------------------------------------------------------
        setup_irq(irq, &c0_compare_irqaction)
       init_mips_clocksource() →
        init_r4k_clocksource() →
        clocksource_register(&clocksource_mips)
        ret = clocksource_enqueue(c [clocksource_mips]) →
        struct list_head *tmp, *entry = &clocksource_list;
        list_add(&c->list, entry);

DEFINE_PER_CPU(struct clock_event_device, mips_clockevent_device);
static LIST_HEAD(clockevent_devices);
static LIST_HEAD(clocksource_list);
DEFINE_PER_CPU(struct tick_device, tick_cpu_device);
static struct clocksource clocksource_mips = {
    .name = "MIPS",
    .read = c0_hpt_read,
    .mask = CLOCKSOURCE_MASK(32),
    .flags = CLOCK_SOURCE_IS_CONTINUOUS,
};

setup_irq(irq, &c0_compare_irqaction)
参考 Request_irq和setup_irq的区别
struct irqaction c0_compare_irqaction = {
    .handler = c0_compare_interrupt,
    .flags = IRQF_DISABLED | IRQF_PERCPU,
    .name = "timer",
};

plat_irq_dispatch →
     do_IRQ(AR7240_CPU_IRQ_TIMER) →
        generic_handle_irq(irq) →
        generic_handle_irq_desc(irq, irq_to_desc(irq)) →
        desc->handle_irq(irq, desc) ==
        handle_percpu_irq() →
        handle_IRQ_event(irq, desc->action) →
        action->handler(irq, action->dev_id) ==
        c0_compare_interrupt() →
        cd->event_handler(cd) ==
        tick_handle_periodic()
Q&A:
SWITCH
1\ Why is there no interrupt signal when the cable is plugged/unplugged from WAN interface?

There are two method to get the cable's state, one is polling and the other is interrupt.
On pb92-router, polling is used. Here is the function follow.
athr_gmac_timer_func() → athr_gmac_poll_link() → athr_gmac_get_link_st() → phy->is_up() …
On ap99-router, interrupt is used. Here is the function follow.
athr_gmac_link_intr() → ar7240_s26_intr() → athr_gmac_check_link() → athr_gmac_fast_reset() →
athr_gmac_hw_setup() → athr_gmac_mii_setup() …

NOTICE: when use interrupt, athr_gmac_link_intr() gets the parameter, and its name is always eth1 and mac->mac_unit is 1, no matter the cable is plugged/unplugged in/from WAN interface or LAN interface.

2\ BUG(ap99) When AP99 WAN VLAN is enabled, then if you “ping 192.168.68.170 –s 1469”, you can NOT get reply. The pc whoes ip is 192.168.68.170 is connected to WAN.

We need to set the Out-of-range bit for register ATHR_GMAC_FIFO_CFG_5 for GMAC0.

OTHERS:(1514(no-vlan) 1518(vlan))
//for board
ifconfig eth0 up
vconfig add eth0 8
ifconfig eth0.8 192.168.1.2 up

//for pc
ifconfig eth4 0.0.0.0
vconfig add eth4 8
ifconfig eth4.8 192.168.1.28 up

ping 192.168.1.28 -s 1472

MORE
ifconfig eth0 mtu 1536

3\ BUG(pb92) ping from pc1 to pc2 does not work.

Maybe the switch chip does not support the feature about IVL(IVL: Independent VLAN Learning; SVL:Shared VLAN Learning). And at present, we disable the learn function for all ports. Here is the code change. For function int athrs16_reg_init(void *arg) in file phys/athrs16_phy.c.

#if HYBRID_VLAN_COMMUNICATE
/* Disable learning function, in order to communicate between
different vlan through br0.
* This will cause duplicate package.
* Because s16 does not support the feature of IVL(Independent VLAN
Learning).
* The code will be removed when the new hardware is used.
*/
printk("Disable switch learning function.\n");
athrs16_reg_write(PORT_CONTROL_REGISTER0,
athrs16_reg_read(PORT_CONTROL_REGISTER0)&(~(0x1<<14)));
athrs16_reg_write(PORT_CONTROL_REGISTER1,
athrs16_reg_read(PORT_CONTROL_REGISTER1)&(~(0x1<<14)));
athrs16_reg_write(PORT_CONTROL_REGISTER2,
athrs16_reg_read(PORT_CONTROL_REGISTER2)&(~(0x1<<14)));
athrs16_reg_write(PORT_CONTROL_REGISTER3,
athrs16_reg_read(PORT_CONTROL_REGISTER3)&(~(0x1<<14)));
athrs16_reg_write(PORT_CONTROL_REGISTER4,
athrs16_reg_read(PORT_CONTROL_REGISTER4)&(~(0x1<<14)));
athrs16_reg_write(PORT_CONTROL_REGISTER5,
athrs16_reg_read(PORT_CONTROL_REGISTER5)&(~(0x1<<14)));
#endif

4\ How to get registers' info for GMAC0 & GMAC1 and Switch core info for each port and phy?
        case ATHR_PHY_RD:
        if( ethcfg->portnum == 0xf){
        int i;
        for(i=0; i<0x10; i++){
        printk("reg %x = %x \n", ethcfg->phy_reg, athr_gmac_reg_rd(mac,ethcfg->phy_reg));
        ethcfg->phy_reg += 4;
        }
        /*
        * ifconfig -i eth1 -p 0xf offset
        * Read GMAC1(eth1) and GMAC0's register info
        */
        }
        else if (ethcfg->portnum != 0x3f) {
        ethcfg->val = phy->read_phy_reg(phyBase,
        ethcfg->portnum, ethcfg->phy_reg);
        /*
        * Read phy's info from switch core
        */
        } else {
        int i;
        for(i=0; i<0x20; i++){
        printk("reg %x = %x \n", ethcfg->phy_reg, phy->read_mac_reg(ethcfg->phy_reg));
        ethcfg->phy_reg += 4;
        }
        ethcfg->val = phy->read_mac_reg(ethcfg->phy_reg);
        /*
        * ifconfig -i eth1 0x20100
        * Read switch's port 1's MIB info
        * [0x20000 + ((i + 1) << 8)]
        */
        }
        break;

OTHER
How to configure?
brctl addbr br0
ifconfig eth0 startvlan
ifconfig eth0 addports 1 27
ifconfig eth0 addports 5 5
ifconfig eth0 setmode 2 0
ifconfig eth0 setmode 1 1
ifconfig eth0 setmode 1 2
ifconfig eth0 setmode 1 3
ifconfig eth0 setmode 1 4
ifconfig eth0 setid 1 1
ifconfig eth0 setid 1 3
ifconfig eth0 setid 1 4
ifconfig eth0 setid 5 2
vconfig add eth0 1
vconfig add eth0 5
ifconfig eth0.1 up
ifconfig eth0.5 up
brctl addif br0 eth0.1
brctl addif br0 eth0.5
ifconfig br0 192.168.1.2 up
ifconfig

why there is dup ?
Because the temp variable is not initialized, and the vlan member is wrong. After disable the learn function, the packet received from one port will be broadcast to all other member ports.

TIPS
1\ export DBG_LEVELS=all=DEBUG, mib=DEBUG
2\ endpoint /usr/local/NetIQ
    for first time using: cp endpoint.ini.newest endpoint.ini
3\ ifconfig eth0
        RX packets:29726 errors:0 dropped:0 overruns:0 frame:0
        TX packets:30260 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:100
        RX bytes:2706612 (2.7 MB) TX bytes:17142433 (17.1 MB)
these info comes from /proc/net/dev, and this file is filled by function .ndo_get_stats.
内核中在文件net/core/dev.c中，函数dev_seq_printf_stats
其中TX overruns: 对应stats.tx_fifo_errors，该参数在ethernet驱动的函数athr_gmac_handle_tx_full中设置。

在文件 busybox/networking/interface.c中读文件 /proc/net/dev
函数： get_dev_fields()
其中TX overruns: 对应/proc/net/dev中的fifo栏。

4\ tcpdump -i eth0 -e
5\ p4 sync ...@CL number //change to one directory
6\ mips-linux-gcc build/gcc-4.3.3/build_mips/staging_dir/usr/bin
7\ delete all the empty line :g/^s*$/d
8\ 250HZ, 则jiffies 每4ms增加1，也即每4ms产生一次系统时钟中断
9\ iperf -s -i 2 -u -p 2000
    iperf -c 192.168.1.2(the peer) -i 2 -u -p 2000 -b 5M -t 1000 -l 22

    iperf -c 239.1.1.1 -u -B 192.168.1.110 -t 20000 -i 1
    iperf -s -B 239.1.1.1 -u -i 1

    hyctl setmc hy0 state disable
10\ error: libipc.so: cannot open shared object file
      export LD_LIBRARY_PATH= …
11\ sudo iperf -u -c 192.168.1.18 -t 30000 -i1 -b 1000M

12\
1、 在web页面上设置 static WAN connect
       17.1.1.1
       255.255.255.0
       GATEWAY: 17.1.1.10
2、 在WAN侧PC设置
       ifconfig eth0 17.1.1.10

3、 在LAN侧PC添加一条路由
      sudo ip router add 17.1.1.0/24 via 192.168.0.1 dev eth4
      sudo ifconfig eth4 192.168.0.10

4、在17.1.1.10上 sudo iperf -s -i 2 -u -p 2000
      在192.168.0.10上， sudo iperf -c 17.1.1.10 -p 2000 -i 2 -u -b 20M -l 22

13\ 发包工具
      Ostinato
     http://code.google.com/p/ostinato/wiki/Downloads?tm=2

14\ 删除一个文件中的多余项
     cat file | sort | uniq > file2
     vi :%s/^/”/g

15\
#!/usr/bin/env python
import os, sys

headfiles = ["pthread.h","semaphore.h","sys/user.h"]

include = "include"
d = {}
for root, dirs, files in os.walk(r'.'):
    for name in files:
        wholes = os.path.join(root,name)
        fd = open(wholes)
        all = fd.read()
        fd.close()
        lst = all.split('\n')
        for i in lst:
        if include in i:
        for j in headfiles:
        if j in i:
        d.setdefault(j, []).append(wholes)
for key in d:
    print "%s: %s"%(key, d[key])

16\ ln -s mv.sh symbol

17\
Edit /etc/resolv.conf
Replace search item with
search users.atheros.com global.atheros.com qca.qualcomm.com na.qualcomm.com qualcomm.com atheros.com

18\
iproute2主要实现了高级路由和流量的控制，而iptable基于内核的netfilter架构实现了防火墙的功能。两者可以配合使用。比如，iptables对包做mark,而iproute2基于mark做响应的处理。

19\ 为什么怎么改u-boot的参数都不是新编译的板子的参数呢？难道是头文件的问题？
最后结果为：不是头文件的问题，而是因为板子上有一个64k(u-boot-env)分区，应该是所用的那块板子保存过以前的某个target的u-boot参数，而仅仅更新u-boot不会擦写该分区。因此，遇到此情况，需要先擦除u-boot-env分区(erase 0x9f040000 +0x10000 [1个扇区])，然后重新更新u-boot.

20\
[ 下面两条不需要了，连接内网的接口的网关配置为另一块网卡的IP地址
ip route del default
ip route add default via 10.235.14.67 dev eth1
]
sudo echo 1 > /proc/sys/net/ipv4/ip_forward
sudo iptables -t nat -I POSTROUTING -j MASQUERADE

网关设置为做为路由器的电脑的IP，同时修改/etc/resolv.conf，添加nameserver

21\
用ubuntu 10.04 架设网关、DHCP

[双网卡地址]
修改/etc/network/interfaces
auto lo
iface lo inet loopback

auto eth1
iface eth1 inet static
address 10.235.14.67
netmask 255.255.252.0
gateway 10.235.12.1

auto eth0
iface eth0 inet static
address 192.168.1.10
netmask 255.255.255.0

[NAT]网关服务
1. 修改/etc/sysctl.conf
   net.ipv4.ip_forward=1
   net.ipv6.conf.all.forwarding=1
2. 执行
   sudo iptables -t nat -A POSTROUTING -s 192.168.1.0/24 -j MASQUERADE
   //sudo iptables -A FORWARD -p tcp --syn -s 192.168.1.0/24 -j TCPMSS --set-mss 1156
   sudo iptables-save > iptables-rules
   sudo mv iptables-rules /etc/iptables-rules
   上面的第一条规则是把所有局域网的请求，都转发到外网
   第二条规则跟网关无关，是为VPN写的。
3. 修改/etc/rc.local启动脚本，加入：
   sudo iptables-restore < /etc/iptables-rules

[DHCP]
1. 安装软件包：
   sudo apt-get install dhcp3-server
2. 修改/etc/default/dhcp3-server配置文件
   INTERFACES="eth0"
3. 修改/etc/dhcp3/dhcpd.conf配置文件
   option domain-name “user.atheros.com global.atheros.com qca.qualcomm.com”
  option domain-name-servers 162.105.129.27, 162.105.129.26, 202.112.7.13;
  subnet 192.168.1.0 netmask 255.255.255.0{
  range 192.168.1.2 192.168.1.200;
  option subnet-mask 255.255.255.0;
  option routers 192.168.1.10;
  }
  1. 重启dhcp服务
    sudo /etc/init.c/dhcp3-server restart

限制某台电脑上网：
sudo iptables -A FORWARD -m mac –mac-source 70:5A:B6:8D:50:F0 -j DROP

批量开启某些电脑上网：
iptables -P FORWARD DROP
for mac in $(cat ipaddressfile); do
    iptables -A FORWARD -m mac --mac-source $mac -j ACCEPT
done

22\
for example, let's set the ageing_time 20 minutes.
~ # echo 120001 > /sys/devices/virtual/net/hy0/bridge/ageing_time

23\ How to enable plc flow control
If you don't have AVitar from v5.2.3 RC6, please take it from the below location,

\\10.12.33.131\CHN_PLC_Server\firmware\7400\v5.2.3-0\RC6\RELEASE\AVitar

And here is the procedure to enable Flow control in PIB,

1) open AVitar-> Go to "Interface configuration" tab-> Click on "Ethernet Override defaults"-> Uncheck " Disable Tx Flow Control" & "Disable Rx Flow Control"
& go back to "Configuration" tab and click on "Write" button, so that the PIB is written to enable flow control.

Let me know if you have questions.

BTW, did you try with 020/011 boards and how was the performance?

Regards,
Natraj

24\
/proc/sys/net/core/wmem_max
/proc/sys/net/core/wmem_default

/proc/sys/net/core/rmem_max
/proc/sys/net/core/rmem_default

25\
问题描述：
STA(192.168.1.118) <----WIFI-----> AP(192.168.1.8) <-------ethernet--------->PC(192.168.1.18)
On STA
ping -s 65500 192.168.1.8 //working 直接由AP的内核做处理，与上层的socket无关
ping -s 65500 192.168.1.18 //working
On AP
ping -s 65500 192.168.1.118 // Not working 这里与上层的socket有关
ping -s 65500 192.168.1.18 //working
On PC
ping -s 65500 192.168.1.8 //working
ping -s 65500 192.168.1.118 //working

为什么有线大包可以ping通，而无线却不行呢？

有个公式：
108544／1024 ＝ 106KByte *2 = 212 Kbyte/4KByte = 53 * 1500 = 79500Byte
说明: 108544来自 cat /proc/sys/net/core/rmem_max
        1024 = 1K
        2 参考下面的知识点 b
        4K for WLAN driver, 因为在wlan driver 中有，
   #define IEEE80211_MAX_MPDU_LEN (3840 + IEEE80211_CRC_LEN + \
    (IEEE80211_WEP_IVLEN + IEEE80211_WEP_KIDLEN + IEEE80211_WEP_CRCLEN))
        1500 平均每个包的大小

问题的突破口：在文件net/core/skbuff.c中，函数__alloc_skb中，有
skb->truesize = size + sizeof(struct sk_buff);
比如，在ethernet driver中，
skb = dev_alloc_skb((ATHR_GMAC_RX_BUF_SIZE + 2 + frame_sz) + L1_CACHE_BYTES – 1);
size == (ATHR_GMAC_RX_BUF_SIZE + 2 + frame_sz) + L1_CACHE_BYTES – 1
所以设想，如果在ethernet driver中，把所传如的size 加大3倍，那么，上面1.8 ping 1.18应该也不work.
经验证，假设成立
如果上面的假设成立，那么需要解决的一个问题是:
skb->truesize 如何和 sk->sk_rcvbuf 建立联系？即内核是如何把收到的包传给应用层的socket?
因此，来到这里net/core/sock.c
int sock_queue_rcv_skb(struct sock *sk, struct sk_buff *skb)
{
    int err = 0;
    int skb_len;
    /* Cast sk->rcvbuf to unsigned... It's pointless, but reduces
       number of warnings when compiling with -W --ANK
     */
    if (atomic_read(&sk->sk_rmem_alloc) + skb->truesize >=
        (unsigned)sk->sk_rcvbuf) {
        err = -ENOMEM;
        goto out;
    }
…....
skb_set_owner_r(skb, sk);
…...

知识点：
a\ AP 上运行的ping代码位于busybox中，networking/ping.c
    /* set recv buf for broadcast pings */
    sockopt = 48 * 1024;
    setsockopt(pingsock, SOL_SOCKET, SO_RCVBUF, (char *) &sockopt,
        sizeof(sockopt));
b\ 该setsockopt 会调用到内核文件net/core/sock.c
    case SO_RCVBUF:
        /* Don't error on this BSD doesn't and if you think
        about it this is right. Otherwise apps have to
        play 'guess the biggest size' games. RCVBUF/SNDBUF
        are treated in BSD as hints */
        @sk_rcvbuf: size of receive buffer in bytes
        if (val > sysctl_rmem_max)
        val = sysctl_rmem_max;
set_rcvbuf:
        sk->sk_userlocks |= SOCK_RCVBUF_LOCK;
        /*
        * We double it on the way in to account for
        * "struct sk_buff" etc. overhead. Applications
        * assume that the SO_RCVBUF setting they make will
        * allow that much actual data to be received on that
        * socket.
        *
        * Applications are unaware that "struct sk_buff" and
        * other overheads allocate from the receive buffer
        * during socket buffer allocation.
        *
        * And after considering the possible alternatives,
        * returning the value we actually used in getsockopt
        * is the most desirable behavior.
        */
        if ((val * 2) < SOCK_MIN_RCVBUF)
        sk->sk_rcvbuf = SOCK_MIN_RCVBUF;
        else
        sk->sk_rcvbuf = val * 2;
        break;

那么内核中，为什么要加 sk->sk_rcvbuf 和 skb->truesize呢？ 解释：限制每个SOCKET的SKB数量，防止过渡使用内存。

引出一个问题： IP 分包是组装好之后，一次发给上层应用的吗？ 是的。

26\
ethtool -s eth0 speed 10 duplex full autoneg off

27\ GPIO的配置 for switch control LED

for example, GPIO 14 control's the led of port1(phy0)
mm 0xb8040000 0x0021930b // GPIO 14 output, set bit14 0
mm 0xb8040038 0x290000 //set GPIO 14 function, ethernet switch link indicator LED.

28\ Push Button

Push Button 使用GPIO中断，其设置在内核代码：
arch/mips/atheros/gpio.c 中 //这里atheros的选择根据宏CONFIG_MACH_AR934x决定。

在gpio.c中，申请／注册中断，设置中断回调函数。

中断回调函数通过函数 register_simple_config_callback设置，现在在无线和有线驱动中都有调用，其中在无线驱动中的文件为： os/linux/src/ath_linux.c, 注册的回调函数是: jumpstart_intr(), 这里通过rtnetlink socket 发送消息到文件apps/athr-hostap/src/drivers/driver_atheros文件中的函数atheros_wireless_event_wireless_custom(); 在有线驱动中的文件为：athrs_mac.c,注册的回调函数是：pushbutton_intr().通过rtnetlink socket 发送消息到文件 ./gateway/services/plc/plcserv/hostsrv/plchostsrv.c +391.

watchdog 的timer寄存器会不停地重新更新，该代码在文件 arch/mips/atheros/934x.c 的函数ath_aphang_timer_fn() 中。

另外，硬件的watchdog定时器是在934x.c中设置的，会调用wdt.c中的函数：ath_set_wd_timer()和ath_set_wd_timer_action().

29\ 插拔网线的event流

Enet:0 port0 up
---eth0.5, flag 1103 //不管是netif_carrier_on 或者 netif_carrier_off ，if (dev->flags & IFF_UP) 该条件都为 TRUE。然后 call_netdevice_notifiers(NETDEV_CHANGE, dev); 掉用 netdevice通知链
---hy_device_event, eth0.5 here // hy_bridge 模块的通知链回调函数为hy_device_event
----hy_port_carrier_check---- 1 br->dev hy0, dev eth0.5
----hy_port_carrier_check---- 3 br->dev hy0, dev eth0.5 //通过NETDEV_CHANGE分支，进入函数hy_port_carrier_check，当网线插上时，netif_carrier_ok(dev) TRUE
hy0: port 2(eth0.5) entering learning state //当netif_carrier_ok(dev) TRUE时，hy_stp_enable_port(p)--> hy_port_state_selection(p->br)-->hy_make_forwarding(p) 在这里启动timer: forward_delay_timer 执行函数 hy_forward_delay_timer_expired
---hy_forward_delay_timer_expired----
hy0: port 2(eth0.5) entering forwarding state
547.06 HYDR hyManager debug: ENTER hyManagerReadBufCB
##############
547.06 HYDR hyManager dump : hyMangerOnLinkStatusChange: Create event: LINK UP
547.06 HYDR hyManager debug: ENTER hyManagerReadBufCB

Enet:0 port:0 down
---eth0.5, flag 1103
---hy_device_event, eth0.5 here
----hy_port_carrier_check---- 2 br->dev hy0, dev eth0.5
----hy_port_carrier_check---- 3 br->dev hy0, dev eth0.5
hy0: port 2(eth0.5) entering disabled state
550.06 HYDR hyManager debug: ENTER hyManagerReadBufCB
##############
550.06 HYDR hyManager dump : hyMangerOnLinkStatusChange: Create event: LINK DOWN
550.06 HYDR hyManager debug: ENTER hyManagerReadBufCB

net/8021q/vlan_dev.c

30\ VLC 设置

  服务器端： RTP(RTP /MPEG Transport Stream)流， 239.1.1.2, 5004, ttl=5,
   clear Activate Transcoding
   Video – MPEG-2 + MPGA(TS)

  sudo ip r add 239.1.1.2 via 192.168.0.18
  sudo ip r add 10.21.5.32 via 10.21.29.177

  客户端： rtp://239.1.1.2:5004
  router路由器页面上：使能igmp snooping 或者 disable igmp snooping

在服务器上安装pimd软件，否则桥上的snooping表会超时。

31\ 关于negotiate后，PHY的速率问题
  ~ # ethreg -p 0x1 0x11 //Phy1 connects to swtich(100Mbps)
Read Reg: 0x00000011 = 0x00007c10
~ # ethreg -p 0x3 0x11 //Phy3 connects to a PC(1000Mbps)
Read Reg: 0x00000011 = 0x0000bc10

32\ 关于PKT lost issue
1\
Hi Kai,

This resolve the pkt lost in my case
CL#1037649 + ATH_GMAC_RX_PKT_CNT=100

Thanks
-Mark T

33\ 关于gmac0／gmac1 FLOW CONTROL
其设置寄存器是 0x19000000/0x1A000000 bit[4] for TX, bit[5] for RX

同时注意寄存器 0x19000050/0x1A000050

the flow control register for s17 switch is 0x7c/0x80/0x84/0x88...

Because the CPU is busy processing business(100% sys usage), and there is no more RX ring for the GMAC's RX DMA to transfer the data that in rx fifo, then rx fifo is full and there will be pause frame. Switch's port0 receives the pause frame, and stops to send data frame, then port0's rx fifo will be full and then there is another pause frame ...
[Ranga] You are right. Provided, you enabled the flow control on phy port also. If not enabled, it would go silent.

在phy的配置中有宏设置：
#define S17_ADVERTISE_ALL ( S17_ADVERTISE_ASYM_PAUSE | S17_ADVERTISE_PAUSE | \
        S17_ADVERTISE_10HALF | S17_ADVERTISE_10FULL | \
        S17_ADVERTISE_100HALF | S17_ADVERTISE_100FULL)

该宏用来设置寄存器：
#define S17_AUTONEG_ADVERT 4

Then use this command to read the pause frame counter:
ethreg -p 0x3f 0x1X58 // for example, ethreg -p 0x3f 0x1258

34\ hyd
hyd 所使用的/tmp/hyd.conf什么时候生成？ 在hy代码中生成，其作为masterd的一个servicePlugin
Hcp: hybrid control protocol
       该模块的作用： contruct and dispatch hybrid control protocol packets

hdtable 通过netlink调用生成，它是根据什么来建立hd表的呢？
1、 在桥上有一个hash表，br->hash_hd[], 通过mac地址的hash值进行索引。
2、 通过函数 hdtbl_create()调用，建立表项，有两个netlink命令字可以调用到该函数，分别是：HYCTL_ADD_HDTBL_ENTRIES 和 HYCTL_UPDATE_HDTBL_ENTRIES, (同时有辅助操作命令字：HYCTL_DEL_HDTBL_ENTRIES, HYCTL_DEL_HDTBL_ENTRIES_BYID, HYCTL_FLUSH_HDTBL)
3、 关于命令字 HYCTL_ADD_HDTBL_ENTRIES 调用过程：
a\ 首先关注数据结构 __hdtbl_entry, 在内核头文件include/linux/if_hybrid.h中。

b\ 在应用层调用流程（在ps模块中调用）：
函数： psChooseDefaultInterfaces()
ps 遍历td表，根据td表中挂接的bridge 和 pc MAC 分别调用下面的函数
bridgeAddHDTableEntries()

其中表项
mac_addr: 为bridge 和 pc MAC
ID: 为所在设备的bridge的MAC

ps – 使用td 模块建立 hd table
ps – 根据pc 模块（pce, pcp, pcw）所取得的参数来管理路径的选择
        参考: pceService_GetLinkCapacityEx()

hatable entry的产生/删除流程
1、hatable的表项
     mac_addr: the stream's dest address, 该mac地址与hd中的mac_addr相同。
     ID： 拷贝自hd表项的ID。
2、函数 hy_hatbl_insert()
     函数： hy_ps_deliver()，ha表项在该函数中加入

HY_TCP_SP:使tcp ack包沿着同一条路径返回，不要参加选路
目前： HybridMode =＝ HY_BRIDGE_MODE_RELAY_OVERRIDE 为HR
ALLMULTI： 清空内核某个接口的mclist，使得所有组播包都可以通过

35\ md 0xb8060008
可以用来判断本次重启是由于watchdog超时，还是正常重启。。。。
如果是watchdog超时，那么最高位为1。

36\ perl p4_integrate.pl

sw/tools/p4_perl
export P4CLIENT=newma_one
perl p4_integrate.pl newma_one 9.3.2 -check -to ***
perl p4_integrate.pl pazhang_hyfi_dev 9.5.3 -check -cl 1503104 1502581 1501465 1500324 1489418 1487635 1487634 1503615

37\ 使用BDI调式reh132驱动

a\ 擦除uboot 分区 ( erase 0x9f000000 +0x100)
b\ 连接好BDI, 给BDI上电，telnet BDI, 设置好配置文件，server ip
    config bdi_wah132.cfg 192.168.1.10
c\ 给板子上电，等待BDI配置正常
d\ 烧写uboot
    load 0xa0001100 u-boot.bin bin
    load 0xa1000000 spi_wah132.bin
    b 0xa1000920
    go
    (wait until BDI enter debug mode)
e\ reset BDI
f\ go 0x9f000000 //板子通过BDI控制，正常启动

1\ Erase the uboot partition (erase 0x9f000000 +0x100),
2\ Connect the BDI to the board and power up, do the necessary configuration(the cfg file, serverip etc.),
3\ Power up the board and wait until the BDI works properly,
4\ Reflash the uboot,
     for example,
     load 0xa0001100 u-boot.bin bin
     load 0xa1000000 spi_wah132.bin
     b 0xa1000920
     go
5\ reset BDI
6\ set the breakpoint if you need to debug
7\ go 0x9f000000

38\ GMAC包过虑寄存器
md 0xba000058
md 0xba00005c // 修改该寄存器可以使某些符合条件的包通过 mm 0xba00005c 0x000e6be6

 39\ 内核编译时配置文件的生成，
a\ 拷贝arch/mip/configs/***_defconfig
b\ 根据arch/mips/Kconfig 调整文件.config

40\ 在linux下改变网卡的速率
     ethtool -s eth4 speed 100 duplex full autoneg off
     ethtool -s eth4 speed 10 duplex half autoneg off
     ethtool -s eth4 autoneg on

41\ Openwrt
./include/kernel-defaults.mk:109:	echo "# CONFIG_KALLSYMS_ALL is not set" >> $(LINUX_DIR)/.config.target
Kernel: build_dir/linux-ar71xx_generic/linux-3.3.8
wifi: qca/feeds/qca/net/qca-wifi

Openwrt中不同的分支版本，一种是最新版但不是最稳定，也就是trunk版，一种是相对稳定版，backfire版。

通过svn从brandkfire获得backfire源代码（此版本意思是从trunk分支的补丁也在backfire版本中了，即包含修复补丁）：
mkdir OpenWrt/
cd OpenWrt/
svn co svn://svn.openwrt.org/openwrt/branches/backfire（回车后等待下载）

注解: 上述svn命令将在当前目录创建一个 OpenWrt/backfire/ 子目录，此目录包含此命令获取到的源代码。您也可以通过下述命令，下载不含修复补丁的backfire的原版源码：
svn co svn://svn.openwrt.org/openwrt/tags/backfire_10.03

如果你用的是backfire版本的源码：
cd OpenWrt/backfire/
svn up
./scripts/feeds update -a
./scripts/feeds install -a

下一步是检查编译环境，若可进行编译则生成默认配置：
make defconfig
若defconfig回显提示缺少软件包或编译库等依赖，则按提示安装所缺软件包或库等即可，不难的，细心点就行。
Menuconfig
Menuconfig is a text-based tool which handles the selection of target, packages to include in the build, kernel options

etc.
make menuconfig

42\
tail -f /var/log/messages //查看DHCP分配的IP.

43\ iperf send multicast

iperf -s -u -p 5001 -B 225.0.0.1 -i 1
iperf -c 225.0.0.1 -u -B 192.168.0.190 -t 10000 -i 1

44\

ccollab login http://ulysses:8080 paulz

45\ 编译AT&T的版本
make -f Makefile.hyb BOARD_TYPE=reh132 VENDOR_CONFIG_DIR=att RELEASE_VER=x?

46\
services/plc/plcserv/hostsrv/FwPibInfo.h

47\ tftp has problem
sudo /etc/init.d/xinetd restart

48\ igmp snooping for s17
ethreg -p 0x3f 0x624=0x017f7f7f //IGMP_JOIN_LEAVE_DP
ethreg -p 0x3f 0x620=0x000000f0
ethreg -p 0x3f 0x618=0x1f78002b //IGMP_JOIN_NEW_EN

ethreg -p 0x3f 0x214=0x01070707
ethreg -p 0x3f 0x210=0x07070707

ethreg -p 0x3f 0x664=0x00040018
ethreg -p 0x3f 0x670=0x00040018
ethreg -p 0x3f 0x67c=0x00040018
ethreg -p 0x3f 0x688=0x00040018
ethreg -p 0x3f 0x694=0x00040018
ethreg -p 0x3f 0x6a0=0x00040018
ethreg -p 0x3f 0x6ac=0x00040018

49\ igmp snooping for s27 (db12x-nand)
ethreg -p 0x3f 0x104=0x00304404 //???
ethreg -p 0x3f 0x204=0x00304404
ethreg -p 0x3f 0x304=0x00304404
ethreg -p 0x3f 0x404=0x00304404
ethreg -p 0x3f 0x504=0x00304404
ethreg -p 0x3f 0x604=0x00304404
ethreg -p 0x3f 0x3c=0xcf48084e
ethreg -p 0x3f 0x2c=0xfe7f017f

50\ ebtables -t nat -A PREROUTING -i eth1 -p 0x88e1 -s ff:ff:ff:f
f:ff:ff -j dnat --to-dst 00:03:7F:11:25:CA

51\
grep -rl VarList ./ |xargs sed -i 's/VarList/va_list/g'

52\ 启动plchost
plchost -i br-lan -l eth0 -N /usr/share/plcfw/QCA7420.nvm -P /tmp/user.pib -s /var/run/plc_socket_server -R -M 2 &

53\ 关于使用dts
a\ 建立dts文件, dts文件格式
   ??

b\ 使用工具转换成dtb文件
build_dir/linux-ar71xx_generic/linux-3.3.8/scripts/dtc/dtc -I dts -O dtb -o reh132.dtb ./target/linux/ar71xx/reh132.dts

c\内核如何使用
  * 添加配置选项：
     CONFIG_ATH79_MACH_GENERIC_DT=y
     CONFIG_MTD_OF_PARTS=y
  * 启动参数
     fdt=0x81000000
  * 在驱动中添加相应的代码，比如：
     +#ifdef CONFIG_OF
     +#include <linux/of_platform.h>
     +#endif
  * 主要改动的文件
     http://qca-git01.qualcomm.com/#/c/1825/

参考： http://hi.baidu.com/zengzhaonong/item/d87ea729f032c285af48f581

54\
grub-install --root-directory=/media/... /dev/sda

问题：PlatformData的整体数据结构是怎么样的？
struct platform_device

54\
tar -xvf *.tar.bz2
tar -jcvf *.tar.bz2 dir/

55\
For aph131:
eth0: eth-cfg = <0x00000012>; /* MII_GE0_SLAVE | MII_GMAC0 */
eth1: ar8033PHY: 修改寄存器 0xb8050048
        1000M : 0x3000000
        100M: 0x101
        10M: 0x1313

For reh132:
注意设置：eth-sw-cfg = <1 0>; /* phy4_mii_en phy_poll_mask */
s27内部的设置，
For aph126/128
bi-port6-cfg = <1 2 0 0 1>; /* force_link speed:1G txpause rxpause duplex */
bi-pad6-cfg = <6 0 0 0 1 1 1 2 0 0>; /* mode rxclk_sel txclk_sel pipe_rxclk_sel txclk_delay_en
   rxclk_delay_en txclk_delay_sel rxclk_delay_sel sgmii_txclk_phase_sel sgmii_rxclk_phase_sel */

56\ mount ubifs

第一次：（如：挂载mtd2）

1、ubiformat /dev/mtd2 -q -e 0
2、ubiattach /dev/ubi_ctrl -m 2
3、ubimkvol /dev/ubi0 -s 220MiB -N app
4、mount -t ubifs ubi0_0 /mnt/app/

以后： （如：挂载mtd2）

1、ubiattach /dev/ubi_ctrl -m 2
2、mount -t ubifs ubi0_0 /mnt/app

57\ initrd – > ramfs – > tmpfs – > initramfs
http://blog.linux.org.tw/~jserv/archives/001954.html

传统的ramdisk是个块设备，要用mkfs来格式化它，才能真正地使用它；而tmpfs是一个文件系统，并不是块设备，只是安装它，就可以使用了。tmpfs是最好的基于RAM的文件系统。

Linux 2.6 kernel提出了一种新的实现机制，即initramfs。顾名思义，initramfs只是一种RAM filesystem而不是disk。initramfs实际是一个cpio归档，启动所需的用户程序和驱动模块被归档成一个文件。因此，不需要cache，也不需要文件系统。

cpio command
Enable these configuration when make menuconfig:
Network --->
    Firewall --->
        <*> ebtables................. Ethernet bridge firewall administration utility
        <*> ebtables-utils........................... ebtables save/restore utilities
Kernel modules --->
   Netfilter Extensions --->
       --- kmod-ebtables................................. Bridge firewalling modules
      <*> kmod-ebtables-ipv4................................ ebtables: IPv4 support
      <*> kmod-ebtables-watchers........................ ebtables: watchers support

Here is the command:
ebtables -t nat -A PREROUTING -p 0x88e1 -d ff:ff:ff:ff:ff:ff -j dnat --to-destination 00:03:7F:11:25:CB

注意： ebtables 在桥上起作用，使用tcpdump时，在eth1上dump的信息为没有nat之前的信息，而在桥上dump到的信息则已经做了修改！

http://blog.csdn.net/zahuopuboss/article/details/8717669

sockaddr_ll, 源文件为<netpacket/packet.h>,结构如下：
struct sockaddr_ll
{
unsigned short int sll_family; /* 一般为AF_PACKET */
unsigned short int sll_protocol; /* 上层协议 */
int sll_ifindex; /* 接口类型 */
unsigned short int sll_hatype; /* 报头类型 */
unsigned char sll_pkttype; /* 包类型 */
unsigned char sll_halen; /* 地址长度 */
unsigned char sll_addr[8]; /* MAC地址 */
};

sll_family 和sockaddr_in中的sa_family一样，但选项要设置为AF_PACKET。
设置成这个选项后，从网卡接收的数据包可以直接传送到应用程序而不经过内核处理。

sll_protocol 表示上层的协议类型：
源文件为<linux/if_ether.h>
/*
* These are the defined Ethernet Protocol ID's.
*/

#define ETH_P_LOOP 0x0060 /* Ethernet Loopback packet */
#define ETH_P_PUP 0x0200 /* Xerox PUP packet */
#define ETH_P_PUPAT 0x0201 /* Xerox PUP Addr Trans packet */
#define ETH_P_IP 0x0800 /* Internet Protocol packet */
#define ETH_P_X25 0x0805 /* CCITT X.25 */
#define ETH_P_ARP 0x0806 /* Address Resolution packet */
#define ETH_P_BPQ 0x08FF /* G8BPQ AX.25 Ethernet Packet*/
#define ETH_P_IEEEPUP 0x0a00 /* Xerox IEEE802.3 PUP packet */
#define ETH_P_IEEEPUPAT 0x0a01 /* Xerox IEEE802.3 PUP Addr Trans packet */
#define ETH_P_DEC 0x6000 /* DEC Assigned proto */
#define ETH_P_DNA_DL 0x6001 /* DEC DNA Dump/Load */
#define ETH_P_DNA_RC 0x6002 /* DEC DNA Remote Console */
#define ETH_P_DNA_RT 0x6003 /* DEC DNA Routing */
#define ETH_P_LAT 0x6004 /* DEC LAT */
#define ETH_P_DIAG 0x6005 /* DEC Diagnostics */
#define ETH_P_CUST 0x6006 /* DEC Customer use */
#define ETH_P_SCA 0x6007 /* DEC Systems Comms Arch */
#define ETH_P_RARP 0x8035 /* Reverse Addr Res packet */
#define ETH_P_ATALK 0x809B /* Appletalk DDP */
#define ETH_P_AARP 0x80F3 /* Appletalk AARP */
#define ETH_P_IPX 0x8137 /* IPX over DIX */
#define ETH_P_IPV6 0x86DD /* IPv6 over bluebook */
#define ETH_P_PPP_DISC 0x8863 /* PPPoE discovery messages */
#define ETH_P_PPP_SES 0x8864 /* PPPoE session messages */
#define ETH_P_ATMMPOA 0x884c /* MultiProtocol Over ATM */
#define ETH_P_ATMFATE 0x8884 /* Frame-based ATM Transport
* over Ethernet
*/

一般是IP的话选ETH_P_IP。或者小心的选择ETH_P_ALL

sll_ifindex 表示接口类型，也可以选择：
源文件<linux/netdevice.h>
/* Media selection options. */
enum {
IF_PORT_UNKNOWN = 0,
IF_PORT_10BASE2,
IF_PORT_10BASET,
IF_PORT_AUI,
IF_PORT_100BASET,
IF_PORT_100BASETX,
IF_PORT_100BASEFX
};
但不知道真的起作用吗，我选的10BASET——基于双绞线的10M以太网。
AF_INET 在<bits/socket.h>里定义为2，表示IP protocol family.
AF_IENT和IF_PORT_10BASET的大小一样。
最好这样得到

   1. int get_nic_index(int fd, const char* nic_name)
   2. {
   3. struct ifreq ifr;
   4. if (nice_name == NULL)
   5. return -1;
   6. memset(&ifr, 0, sizeof(ifr));
   7. strncpy(ifr.ifr_name, nic_name, IFNAMSIZ);
   8. if (ioctl(fd, SIOCGIFINDEX, &ifr) == -1) {
   9. perro("SIOCGIFINDEX ioctl error");
  10. return -1;
  11. }
  12. return ifr.ifr_ifindex;
  13. }

sll_hatype ARP 硬件地址类型
可以选择，
源文件为<net/if_arp.h>
/* ARP protocol HARDWARE identifiers. */
#define ARPHRD_NETROM 0 /* From KA9Q: NET/ROM pseudo. */
#define ARPHRD_ETHER 1 /* Ethernet 10/100Mbps. */
#define ARPHRD_EETHER 2 /* Experimental Ethernet. */
#define ARPHRD_AX25 3 /* AX.25 Level 2. */
#define ARPHRD_PRONET 4 /* PROnet token ring. */
#define ARPHRD_CHAOS 5 /* Chaosnet. */
#define ARPHRD_IEEE802 6 /* IEEE 802.2 Ethernet/TR/TB. */
#define ARPHRD_ARCNET 7 /* ARCnet. */
#define ARPHRD_APPLETLK 8 /* APPLEtalk. */
#define ARPHRD_DLCI 15 /* Frame Relay DLCI. */
#define ARPHRD_ATM 19 /* ATM. */
#define ARPHRD_METRICOM 23 /* Metricom STRIP (new IANA id). */

sll_pkttype 包含分组类型
有效的分组类型：
目标地址是本地主机的分组用的 PACKET_HOST，
物理层广播分组用的 PACKET_BROADCAST ，
发送到一个物理层多路广播地址的分组用的 PACKET_MULTICAST，
在混杂(promiscuous)模式下的设备驱动器发向其他主机的分组用的PACKET_OTHERHOST，
本源于本地主机的分组被环回到分组套接口用的 PACKET_OUTGOING。
这些类型只对接收到的分组有意义。sll_addr 和 sll_halen 包括物理层(例如 IEEE 802.3)地址和地址长度。精确的解释依赖于设备。

sll_halen 为MAC地址长度（6 bytes)
源文件<linux/if_ether.h>
#define ETH_ALEN 6 /* Octets in one ethernet addr */
#define ETH_HLEN 14 /* Total octets in header. */
#define ETH_ZLEN 60 /* Min. octets in frame sans FCS */
#define ETH_DATA_LEN 1500 /* Max. octets in payload */
#define ETH_FRAME_LEN 1514 /* Max. octets in frame sans FCS */

sll_addr[8] 为目的MAC地址（按sockaddr_in.sin_addr为目的IP地址推测）

填充完这个结构后，创建一个SOCKET
sockfd=socket(AF_PACKET,SOCK_RAW,htons(ETH_P_IP));

   1. int set_nic_promisc(int sockfd, const char *nic_name)
   2. {
   3. struct ifreq ethreq;
   4. strncpy(ethreq.ifr_name, nic_name, IFNAMSIZ);
   5. ioctl(sockfd, SIOCGIFFLAGS, &ethreq);
   6. ethreq.ifr_flags |= IFF_PROMISC;
   7. ioctl(sockfd, SIOCSIFFLAGS, &ethreq);
   8. return 0;
   9. }

如果以上步骤成功的话，网卡现在应该处于混杂模式了。